Human-robot handshake
qb SoftHand
The proposed State Machine, works as follows, compute the full closure twice. The first time without the human hand in handshaking position and the second time we are expecting a human hand to be in the position. Both times we are saving the position value sent to the softhand and the corresponding current absorbed by the dc motor [q,i]. This method is safe since the proportional gain(stiffness parameter) is kept at 0,1.

After the 'Calibration Full' state, two vectors with the couples [q,i] are available. Due to the physical presence of the human hand in the second state, the dc motor had to absorb more current but the respective [q] column are identical. Now in order to obtain the residual current which we assume to be proportional to the grasping force, we simply subtract the above mentioned columns [i].
The graph below shows the two current obtained with this configuration, its clear that a physical obstacle in the finger movements is affecting the way current is absorbed.

The last state 'Handshake' is executing the handshake in the following way:
1- Sending the 'first touching position' which is the position in which the residual current is at relatively low value (10% of its total).
2- Scaling the value read from the FSR sensors in order to span the full range of the current handshaking.
3- Setting as maximum closure position, a position in which the residual current obtained after the state 'Calibration Full' is at a relatively high value (80%).

The future work will be to find ways to optimize this Low Threshold and High Threshold.
Currently we have a linear controller with respect to the FSR sensors.
The maximum position that the hand is receiving is 19000 (where the hand is fully closed), that means that we never want out controller to send values up to 19000 in the 'handshake' state.
The range of position which we want to send must vary with respect to the hand size f.i. a small hand will have a starting closing position high. (the qbhand must close itself more in order to touch a small hand). On the other side a big hand will have a low starting closing position, which enables the controller to play more with the ranges. In case of a small hand, as closer the starting position is to the upper threshold 19000 as less effective the controller can be.